End Effector Dynamic Analysis

left lbrace alignl stack { %SIGMA F_x : phantom % P - R_Bx - B_x= 0# %SIGMA F_y : phantom % R_A - R_By - B_y= 0# %SIGMA M_A : phantom % l_AB sin %varphi_1( t ) R_Bx - l_AB cos %varphi_1( t ) R_By - l_Acm sin %varphi_1( t ) B_x - l_Acm cos %varphi_1( t ) B_y = 0 } right none drarrow phantom a left lbrace alignl stack { R_Bx = P - B_x # R_A - R_By = B_y# l_AB tan %varphi_1( t ) R_Bx - l_AB R_By = l_Acm B_y - l_Acm tan %varphi_1( t ) B_x } right none
left lbrace alignl stack { %SIGMA F_x : phantom % R_Bx - R_Cx - sin %varphi_2(t) B_t ^x + cos %varphi_2(t) B_n ^x = 0# %SIGMA F_y : phantom % R_By - R_Cy + F - cos %varphi_2(t) B_t ^y - sin %varphi_2(t) B_n ^y = 0# %SIGMA M_C : phantom % -l_BC cos %varphi_2( t ) R_Bx + l_BC sin %varphi_2( t ) R_By - l_CD sin %varphi_2( t ) F + l_Bcm B_n= 0 } right none
drarrow phantom a left lbrace alignl stack { R_Bx - R_Cx = sin %varphi_2(t) B_t ^x - cos %varphi_2(t) B_n ^x# R_By - R_Cy = cos %varphi_2(t) B_t ^y + sin %varphi_2(t) B_n ^y - F# -l_BC cos %varphi_2( t ) R_Bx + l_BC sin %varphi_2( t ) R_By = l_Bcm B_n - l_CD sin %varphi_2( t ) F } right none

The inertial force vectors were chosen based on the previous analysis of accelerations.

Next we will put the formulas in matrix form so they may be used in Matlab.

left[matrix{ 0#1#0#0#0## 1#0#-1#0#0## 0#l_AB tan %varphi_1( t )#-l_AB#0#0## 0#1#0#-1#0## 0#0#1#0#-1## 0#-l_BC cos%varphi_2( t )#l_BC sin%varphi_2( t )#0#0 }right] left[matrix{ R_A##R_Bx##R_By##R_Cx##R_Cy }right] =left[matrix{ P##0##0##0##-F##-l_CD sin %varphi_2( t ) F }right]+ left[matrix{ -B_x##B_y##l_Acm B_y - l_Acm tan %varphi_1( t ) B_x##sin %varphi_2 ( t ) B_t^x - cos %varphi_2 ( t ) B_n^x##cos %varphi_2 ( t ) B_t^x + sin %varphi_2 ( t ) B_n^y##l_Bcm B_n }right]

To further reduce the number of variables, we may relate the two angles %varphi_1( t ) and %varphi_2 ( t ) .
left lbrace alignl stack{ sin %varphi_1(t) = h over l_AB# sin ( %varphi_2(t) - 90 ) = h over l_BD } right none phantom aaaaa drarrow phantom aaaa l_AB sin %varphi_1( t ) = l_BD cos %varphi_2( t ) phantom aaaaa drarrow phantom aaaa %varphi_2( t ) = arcos left( l_AB over l_BD sin %varphi_1( t ) right)

For a static analysis we may exclude the inertial force matrix. This static analysis is only sufficient for when the gripper mechanism including the arm is stationary. The same applies for the dynamic analysis as any kinematics of the arm aren’t included.

As the clamping strength of the end effector while the arm is in motion is an integral part of contraption, these calculations do not fully represent the behavior of the entire system. The next part of the analysis will include the dynamics of the next three degrees of freedom.