End Effector Static Analysis
We will begin with the static analysis for the end effector.
Since the end effector is symmetrical, we will only consider the top half of the mechanism. To corrugate, our P will need to be one-half the total realistic input force for our mechanism.

left lbrace alignl stack { %SIGMA F_x : phantom % P - R_Bx = 0# %SIGMA F_y : phantom % R_A - R_By = 0# %SIGMA M_A : phantom % l_AB sin %varphi_1( t ) R_Bx - l_AB cos %varphi_1( t ) R_By = 0 } right none phantom aaaaaa drarrow phantom aaaaaa left lbrace alignl stack { R_Bx = P# R_By = R_A# R_By = tan %varphi_1( t ) R_Bx = tan %varphi_1( t ) { P } } right none

left lbrace alignl stack { %SIGMA F_x : phantom % R_Bx - R_Cx = 0# %SIGMA F_y : phantom % R_By - R_Cy + F = 0# %SIGMA M_C : phantom % -l_BC cos %varphi_2( t ) R_Bx + l_BC sin %varphi_2( t ) R_By - l_CD sin %varphi_2( t ) F = 0 } right none phantom aa drarrow phantom aa left lbrace alignl stack { R_Bx = R_Cx# F = R_Cy - R_By# F = l_CD over l_BC left (R_By - ctg %varphi_2( t ) R_Bx right ) } right none

Final formula for the pressing force:
F = l_CD over l_BC left (tan %varphi_1(t) - ctg %varphi_2(t) right ) P

We may observe that the BD element functions as a lever. This may give us a mechanical advantage.

To further increase the pressing strength, we must make tan %varphi_1(t) as large as possible while minimizing ctg %varphi_2(t) . This suggests F is strongest when %varphi_1(t) = 90 ^o and %varphi_2(t) > 90^o where reasonable.

Since this formula was derived for only one-half of the end effector, we need to make a consideration to accommodate the other half. The pressing force P will remain the same, however the pressing force is now shared between two grips. Since the grips are stationary, both pressing forces must be equal and the total force is equivalent to the derived equation.