Rack and Pinion

To select the correct rack and pinion for the x axis linear movement, we will make a few assumptions and calculations.

Mass to be Moved	m = 5 kg
Speed	v = 1 m/s
Acceleration Time	tb = 1 s
Acceleration Due to Gravity	g = 9.81 m/s2
Coefficient of Friction	μ = 0.15
Load Factor	KA = 1
Life-Time Factor	fn = 0.85
Safety Coefficient	SB = 1.1
Linear Load Distribution Factor	LKHβ = 1.1

Calculations:

a = v over t_b = 1 over 1 = 1 m over s^2

F_u = { m * g * %mu + m * a } over 1000 = 12.3575 over 1000 = 0.0123575 kN

Permissible Feed Force assumed at 11.5 kN with ... rack and ....pinion :

F_{u zul./per.} = F_{ u Tab } over { K_A * S_B * f_n * L_{KH %beta} } = 11.5 over 1.0285 = 11.18 kN

Condition:

F_{ u zul./per. } > F_u	11.18kN > 0.0123575kN

With the above condition fulfilled, we know that the rack and pinion will be sufficient for out application.